AROMA BURSA FRUIT JUICES

AND FOOD IND. INC.

Ankara Asfaltı, Gürsu Kavşağı

16580 GÜRSU / BURSA – TURKEY

TEL: +90 –  224 – 3713939 ( 10 LINES )

FAX: +90 – 224 – 3713949 / 50

E-MAIL: aroma@aroma.com.tr

WEB: www.aroma.com.tr

APPLE JUICE CONCENTRATE

Specification No: SP 026 Y

GENERAL DESCRIPTION:

Concentrated apple juice is the unfermented but fermentable product obtained from the edible part of

mature and sound fruits of one or more typical Turkish varieties. Apple Juice Concentrate is natural, clear, homogenous, free from foreign materials, fresh, free from foreign taste and odour, viscous liquid. It is suitable for consumption and is suitable for production of fruit juices and nectars.

MANUFACTURING PROCESS:

Apple juice is obtained from the fruit by mechanical processes and concentrated by the physical removal of a part of the water.

CHEMICAL CHARACTERISTICS:

| ANALYSIS | UNITS | TARGET | MINIMUM | MAXIMUM | METHOD |
| --- | --- | --- | --- | --- | --- |
| °Brix ref. Uncorr.: | °Bx | 70,0 | 69,9 | 70,2 | IFU 8 |
| Titratable Acid | g/kg ( calc. as Malic Acid ) | - | 8 | 18 | IFU 3 |
| Colour Value | 12°Bx, 440 nm, %T | - | 38 | - |  |
| Clarity | 12°Bx, 625 nm, %T | - | 93 | 100 |  |
| Turbidity | 11,2°Bx, NTU | - | - | 5 | IFU Recommendation 7 |
| Patulin | 11,2°Bx, ppb | - | - | 50 | IFU Recommendation 2 |

MICROBIOLOGY:

| Total Plate Count ( OSA ) | CFU / g. | Max. 100 | IFU 2 |
| --- | --- | --- | --- |
| Total Yeast ( OGY ) | CFU / g. | Max. 500 | IFU 3 |
| Total Mould ( OGY ) | CFU / g. | Max. 10 | IFU 4 |
| Alicyclobacillus (BAT) | CFU / 10g. | none | IFU 12 |

STORAGE AND SHELF LIFE:

18 months at ( 0° ) – ( ± 4° ) C.

PACKING AND PRESERVATIVES:

Filled in 285 Kg. sheet iron drums, interior covered with food grade polyethylene bag and non-aseptic bag.

No preservatives added.

QUALITY MANAGER

# Text boxes

UNCONTROLLED COPY

FOR INFORMATION